## Slide 1
Notes: <number>

## Slide 2: ASPECTS:
<number>
  Use of better designed, ICF coaches with better springing arrangements.
  Better breaking system for safe and smoother rail travel.
  Use of diesel and electric traction to carry heavier loads at higher speeds.
  Provision of universal couplers.
  Modern signaling techniques.
  Computerized train reservation system.
Notes: <number>

## Slide 3: MODERNIZATION OF TRACK:
Components of Modernization of Track:
1} Heavier Track Structure:
Heavier and wear resistant rails having more UTS.
Prestressed concrete sleepers.
Long welded rails.
2} Modern methods of track maintenance:
Use of D.T.M , M.S.P methods give better track geometry and smoother rail travel at economical cost.
<number>

## Slide 4
3} Modern methods of track Renewal and Laying:
These includes quick methods of relaying.
4} Modern methods of track inspection and track monitoring:
These include recording instruments, use of computers, ultrasonic testing of rails.
TO GET SPEED OF THE ORDER OF 160 TO 200 kmph THE TRACK WILL HAVE TO BE MAINTAINED TO VERY CLOSE TOLERANCES.
<number>

## Slide 5: LIMITATIONS TO HIGHER SPEED
Adhesion between rails and wheels.
Stability of vehicle on curves and crossings.
Riding comfort of passenger.
Unbalanced acceleration on account of curves.
High standard of maintenance which may be uneconomical.
Increased deformation and stresses in track components so need of heavier track structure.
Elastic structure of railway track gets disturbed in alignment, gauge because of high speed and heavy axle loads.
<number>

## Slide 6: METHODS OF MAINTENANCE
1} Mechanical maintenance:
levelling and alignment of track.
Profiling of ballast section to the requirement.
Changing of defective sleepers.
Use of L.W.R.
Correcting gauge.
This method is effective, economical and efficient to allow the needs of higher speed and higher axle loads.
<number>

## Slide 7
<number>

## Slide 8
2} Directed track maintenance:
Proper identification of defects in track geometry by means of measuring and recording devices.
Rectification of these defects in track geometry at identified locations.
Checking of quality of work and output by supervisor.
This method is more economical because only the portion of track is attended rather than entire track length.
<number>

## Slide 9
3} Ultrasonic Rail flaw detection:
Inspection of track fractures.
4} Improvement of curves:
It is likely to get distorted due to unbalanced loading on inner and outer rail so super elevation is maintained and checked time to time.
5} Drainage of Ballast bed:
Special attention to drainage arrangements are made near points and crossings.
<number>

## Slide 10: TRACK INSPECTION AND RECORDING:
Inspection of track parameters is done by following equipments:
1} Hallade Track Recorder:
Produce a graphic record of various parameters of track.
Placed on levelled base plate in the center of bogie.
Track alignments, sudden sags or humps, lateral oscillations of vehicle due to gauge variation, uneven super elevation etc. are recorded.
Charts so recorded are analysed kilometer wise to assess it properly.
<number>

## Slide 11
2} Amsler track recording cars:
It is a vehicle of express passenger type having 2 bogies.
Gives continuous record of unevenness, twist , gauge, superelevation, alignment.
3} Oscillograph cars:
Mobile laboratory cum instrumental cars having pen type recorders.
Connected to accelerometers and LVDTs.
Assess safety and stability of locomotives and vehicles as well as standard of track maintenance.
<number>

## Slide 12: Brief explanation of recordings
(1.)Twist -When the recording car follows a straight path where both the rails are in one plane, the track of the twist line follows the datum line. On curves, however, the record will be as shown in sketch below.
Change in cross-levels over short length will indicate twist.
<number>

## Slide 13
2.) Gauge - The trace indicates three conditions viz., correct gauge, tight gauge or slack gauge as shown-in Sketch below –
The shift of the mean above the datum line indicates slack gauge as at BC. If the mean follows the datum, it indicates correct gauge as at AB. The shift of the mean below the datum line indicates tight gauge as at D.
<number>

## Slide 14
4) Unevenness- Unevenness is recorded by variation in the top level of each rail. It is normally noticed at joints either low or high. It is necessary to compare the records of both the rails.
Monitoring of the riding quality of track- While the track recording cars can record the track geometry
(i) the Hallade track recorders,
(ii) the Oscillograph car
the portable accelerometers record vertical and lateral accelerations, on which depends, the riding quality.
<number>

## Slide 15: IF TRACK INSPECTION IS NOT DONE
<number>

## Slide 16: TYPES OF MODERN RAILWAYS
MONORAIL:
A monorail is a rail-based transportation system based on a single
rail, which acts as its sole support and its guideway.
<number>

## Slide 17
TUBE RAILWAYS:
An electrically powered railroad with tracks running through a tunnel underground.
<number>

## Slide 18
<number>

## Slide 19
SKY BUS:
THE URBAN TRANSPORT
TECHNOLOGY FOR THE
NEW
MILLENIUM
<number>

## Slide 20
METRO RAIL:
<number>

## Slide 21
<number>
THANK YOU……